## Slide 1: Damping Wrist Joint Tremors with Low Cost Soft Robotics
Technical University of Munich
Chair for Cognitive Systems
Prof. Dr. Gordon Cheng
2022-07-29
For the lecture:
Human-centered Neuroengineering:
Neurorehabilitation
Presented by team 5:
Thien Le
Jose Garcia
Klara Tomaskovic
Benoit Auclair
Supervisors:
Natalia Paredes Acuna, Nicolas Berberich

## Slide 2: Introduction It’s been a long way… Definition of the problem   Detection and attenuation of intention tremors at the wrist joint Concept + model + first rough prototype TENS stimulation trials Definition of the problem   Detection and attenuation of tremors at the wrist joint Second prototype + final design Functional actuation Final prototype Signal processing & control scheme 2 experiments Results & conclusion
Mechanical Design | TuMove |
‹#›
Final presentation
2022-07-29
Project update
2022-07-08
Project update
2022-07-22
Stay tuned

## Slide 3: Mechanical Design
Mechanical Design | TuMove |
‹#›

## Slide 4: Signal Processing y axis of the gyroscope is perpendicular to flexion/extension discrete Fourier transform to perform frequency analysis RMS over tremor-related frequencies and over N sampling periods for robustness
Signal Processing | TuMove |
‹#›
Gyroscope Y-axis
@ 40 Hz
DFT
with N = 16
∆ f = 2.5 Hz
RMS
of DFT coefficients
7.5 - 12.5 Hz
PD Controller
RMS
over the past N=5 samples

## Slide 5: PID controller
Signal Processing | TuMove |
‹#›

## Slide 6: Experiments Free wrist Nine-Hole peg Test
Experimental results | TuMove |
‹#›
Notes: Participant ages from 23 - 36 , 3 male and 2 female

## Slide 7: Results - Experiment 1 Across all 4 subjects and all 3 trials the device showed 48% decrease in spectral energy in the target band Metrics: mean rms of spectral energy over a window of n = 20 samples
Experimental results | TuMove |
‹#›

## Slide 8: Results - Experiment 2
Experimental results | TuMove |
‹#›

## Slide 9: Thanks for listening Summary An IMU-based tremor detection Novel Soft Robotics Actuator Linkage Portable, lightweight, comfortable, and compact unit –> Device damps tremor energy up to 48% of artificial tremor
Q & A | TuMove |
‹#›
Notes: 40 grams heavier than a big Mac.

## Slide 10: Demo Thanks for listening - Q&A
Live demo | TuMove |
‹#›

## Slide 11: References
References | TuMove |
‹#›